    - Measurements

Measurements of background harmonic levels are generally needed for Stage 2 and always needed for Stage 3 assessments.  The responsibility for making these measurements lies with the NOC, but the customer may be required to assist by providing information on the operation of non-linear equipment during the test period, or by ensuring other non-linear equipment is not operating during the test period.  In general, the background harmonics should be assessed over a least a 7 day period when the PCC fault levels are representative of post-connection conditions.  If this is not the case, scaling of the measured levels may need to be carried out in making the assessment.  Note that the minimum period above may not be long enough to characterise the background harmonic levels; these levels can be subject to variation over longer periods due to seasonal and other changes in load pattern and network configuration. The Application Guide ETR 122 considers measurements in more detail.