Proposal for the treatment of connection applications where the existing network background levels, including Total Harmonic Distortion (THD), are above G5/5 Planning Levels but below Compatibility Levels

A new connection or a modification to an existing connection may proceed where the connecting customer can provide mitigation measures to ensure that those Harmonic levels, including THD, which are above the Planning Levels, do not further increase.  For example an individual harmonic order could be increased at the expense of a reduction, or no increase, of a different harmonic order already above the planning limit.   This would represent the minimum cost scheme to provide the new connection or modification to an existing connection.

When proposing mitigation measures for the connection scheme the Network Operator may consider an enhanced scheme of mitigation measures over an above the minimum cost scheme to further reduce the harmonic levels, including THD, to a level at or below the planning level as part of the connection application.